Assignment #14: Electric Circuits

1. The parallel circuit at the right depicts three resistors connected to a voltage source. The voltage source (ΔVtot) is a 110.-V source and the resistor values are 15.4 Ω (R1), 21.9 Ω (R2) and 11.7 Ω (R3). 
a. Determine the current in each branch resistor.
b. Determine the total current in the circuit.			          c. Determine the equivalent resistance of the circuit.

2. Using conventional symbols, add to the circuit diagram below:

-	an ammeter that measures the current through R1

-	a voltmeter that measures the potential difference across R2

- 	a voltmeter that measures the total potential difference

- 	an ammeter that measures the total current in the circuit

3. Voltmeters can be used to determine the voltage across two points on a circuit. An ammeter can be used to determine the current at any given location on a circuit. The circuit below is powered by a 24.0-volt power source and utilizes four voltmeters and three ammeters to measure voltage drops and currents.

The resistor values are 54.5 Ω (R1), 31.7 Ω (R2) and 48.2 Ω (R3). Determine the ammeter readings and voltmeter readings.

4. Determine the equivalent resistance for the circuit in #3.

5. Draw a series circuit with a 30.0 Ω, 40.0 Ω and a 50.0 Ω resistor with a 60.0 V power supply. A) Calculate the equivalent resistance for the circuit.

B) Calculate the current in the circuit.

C) Calculate the potential difference across each resistor.

6. A circuit consists of 2 resistors connected in parallel. The power supply is fixed at 24 V.

A) What is the resistance of resistor 2 if R1 = 12 Ω and the IT = 12 A? Draw the circuit.

B) What is the equivalent resistance?

7. A series circuit is built. It has a power supply at 100.0 V. The value of the resistors are 5.0 Ω, 6.0 Ω and 9.0 Ω. Find the current at each resistor and the equivalent resistance.

8. When a parallel circuit has two branches and each branch has a 10.0 Ω resistor, what is the equivalent resistance?

9. Three branches make up a parallel circuit. On one branch there is a resistor that is 30.0 Ω, and on the other two branches there is a 60.0 Ω on each. The branch with the 30.0 Ω resistor has a current intensity of 6 A.

Draw the circuit.

Find the current readings for the other two branches.

Find the total voltage.

Find the total current.

Find the equivalent resistance.

Assignment #14: Electric Circuits

1. The parallel circuit at the right depicts three resistors connected to a voltage source. The voltage source (ΔVtot) is a 110.-V source and the resistor values are 15.4 Ω (R1), 21.9 Ω (R2) and 11.7 Ω (R3). 
a. Determine the current in each branch resistor.                               7.14 A, 5.02 A, 9.4 A
b. Determine the total current in the circuit.	21.56 A

c. Determine the equivalent resistance of the circuit. 5.1 ohms

2. Using conventional symbols, add to the circuit diagram below:

-	an ammeter that measures the current through R1

-	a voltmeter that measures the potential difference across R2

- 	a voltmeter that measures the total potential difference

- 	an ammeter that measures the total current in the circuit

3. Voltmeters can be used to determine the voltage across two points on a circuit. An ammeter can be used to determine the current at any given location on a circuit. The circuit below is powered by a 24.0-volt power source and utilizes four voltmeters and three ammeters to measure voltage drops and currents.

The resistor values are 54.5 Ω (R1), 31.7 Ω (R2) and 48.2 Ω (R3). Determine the ammeter readings and voltmeter readings. 24.0 V throughout    0.44 A, 0.76 A, 0.5 A

4. Determine the equivalent resistance for the circuit in #3.  14.1 ohms

5. Draw a series circuit with a 30.0 Ω, 40.0 Ω and a 50.0 Ω resistor with a 60.0 V power supply. A) Calculate the equivalent resistance for the circuit. 120 ohms

B) Calculate the current in the circuit. 0.5 A

C) Calculate the potential difference across each resistor. 15V, 20 V, 25V

6. A circuit consists of 2 resistors connected in parallel. The power supply is fixed at 24 V.

A) What is the resistance of resistor 2 if R1 = 12 Ω and the IT = 12 A? Draw the circuit. 2.4 ohms

B) What is the equivalent resistance? 2 ohms

6. A circuit consists of 3 resistors connected in parallel. The power supply is fixed at 24 V.

A) What is the resistance of resistor 3 if R1 = 12 Ω, I1 = 4 A and the IT = 12 A? Draw the circuit.

6 ohms

B) What is the equivalent resistance? 0.5 ohms

7. A series circuit is built. It has a power supply at 100.0 V. The value of the resistors is 5.0 Ω, 6.0 Ω and 9.0 Ω. Find the current at each resistor and the equivalent resistance.  20 ohms, 5 A throughout

8. When a parallel circuit has two branches and each branch has a 10.0 Ω resistor, what is the equivalent resistance? 5 ohms

9. Three branches make up a parallel circuit. On one branch there is a resistor that is 30.0 Ω, and on the other two branches there is a 60.0 Ω on each. The branch with the 30.0 Ω resistor has a current intensity of 6 A.

Draw the circuit.

Find the current readings for the other two branches. 3 A current  throughout

Find the total voltage. 180 V

Find the total current. 3 A current  throughout

Find the equivalent resistance.